WILLIAMSON CORPORATION

70 Domino Drive, Concord, MA 01742

Telephone: (978) 369-9607, Fax: (978) 369-5485, Web Site:  williamsonir.com

Quotation No. ___________

To:	USA and Canadian Representatives	Phone:	(978) 369-9607

Williamson Corporation	Fax:	(978) 369-5485

70 Domino Drive

Concord, MA 01742 USA	Date:	May 6, 2009

CC:

Ref:	Pilot Monitor Quote Form

____________________________________________________________________________________________________________

Unit	Ext.	Estimated

Item	Qty		Part Number							Price	Price	Shipment

Typical Pilot Monitor Configuration with NEMA4X Enclosure

A	  1		PM-35-A-N4							$6,700		stock - 4 weeks

Description:		Dual-wavelength visual aiming pilot monitor with internal display

and user interface, signal conditioning and system diagnostics.

in NEMA-4X (IP65)  housing. Includes sealed junction box

with screw terminals attached to housing for field wiring.

Measuring range:	0 - 100 %

Field of View:		35:1 optics, 28ft  diameter @ 1000ft  distance (8.5m @ 305m )

Sensor Output:		A:  Stand Alone Sensor set to Analog Output. Provides  linear

( field selectable ) 	mA Output and SPST relay output.

( select D  for Stand Alone Sensor set to RS485 Digital Comms for

operation with the  Interface Module accessory, see Options below )

Mounting included:	Swivel Bracket

Input Power:                    Sensor requirements: 24Vdc (300mA)

Pilot Monitor with NEMA4X Enclosure for Closely Spaced Flares or Mounting Distances Greater then 1500ft/457m

B	  1		PM-70-A-N4							$6,900		3 - 4 weeks

Description:		Dual-wavelength visual aiming pilot monitor with internal display

and user interface, signal conditioning and system diagnostics.

in NEMA-4X (IP65)  housing. Includes sealed junction box

with screw terminals attached to housing for field wiring.

Measuring range:	0 - 100 %

Field of View:		70:1 optics, 14ft diameter @ 1000ft distance ( 4.2m @ 305m )

Sensor Output:		A:  Stand Alone Sensor set to Analog Output. Provides  linear

( field selectable ) 	mA Output and SPST relay output.

( select D  for Stand Alone Sensor set to RS485 Digital Comms for

operation with the Interface Module accessory, see Options below )

Mounting included:	Swivel Bracket

Input Power:                    Sensor requirements: 24Vdc (300mA)

Unit	Ext.	Estimated

Item	Qty		Part Number							Price	Price	Shipment

Typical Pilot Monitor Configuration with NEMA7X Enclosure

C	  1		PM-35-A-N7							$7,900		4  - 6 weeks

Description:		Dual-wavelength visual aiming pilot monitor with internal display

and user interface, signal conditioning and system diagnostics.

in NEMA-7  housing. Includes sealed junction box

with screw terminals attached to housing for field wiring.

Measuring range:	0 - 100 %

Field of View:		35:1 optics, 28ft  diameter @ 1000ft  distance (8.5m @ 305m )

Sensor Output:		A:  Stand Alone Sensor set to Analog Output. Provides  linear

( field selectable ) 	mA Output and SPST relay output.

( select D  for Stand Alone Sensor set to RS485 Digital Comms for

operation with the  Interface Module accessory, see Options below )

Mounting included:	Swivel Bracket

Input Power:                    Sensor requirements: 24Vdc (300mA)

Pilot Monitor with NEMA7X Enclosure for Closely Spaced Flares or Mounting Distances Greater then 1500ft/457m

D	  1		PM-70-A-N7							$8,100		4 - 6 weeks

Description:		Dual-wavelength visual aiming pilot monitor with internal display

and user interface, signal conditioning and system diagnostics.

in NEMA 7 housing. Includes sealed junction box

with screw terminals attached to housing for field wiring.

Measuring range:	0 - 100 %

Field of View:		70:1 optics, 14ft diameter @ 1000ft distance ( 4.2m @ 305m )

Sensor Output:		A:  Stand Alone Sensor set to Analog Output. Provides  linear

( field selectable ) 	mA Output and SPST relay output.

( select D  for Stand Alone Sensor set to RS485 Digital Comms for

operation with the Interface Module accessory, see Options below )

Mounting included:	Swivel Bracket

Input Power:                    Sensor requirements: 24Vdc (300mA)

Typical Pilot Monitor Configuration with ATEX Enclosure

E	  1		PM-35-A-ATEX						$8,000		4  - 6 weeks

Description:		Dual-wavelength visual aiming pilot monitor with internal display

and user interface, signal conditioning and system diagnostics.

in CENELEC  housing. Includes sealed junction box

with screw terminals attached to housing for field wiring.

Measuring range:	0 - 100 %

Field of View:		35:1 optics, 28ft  diameter @ 1000ft  distance (8.5m @ 305m )

Sensor Output:		A:  Stand Alone Sensor set to Analog Output. Provides  linear

( field selectable ) 	mA Output and SPST relay output.

( select D  for Stand Alone Sensor set to RS485 Digital Comms for

operation with the  Interface Module accessory, see Options below )

Mounting included:	Swivel Bracket

Input Power:                    Sensor requirements: 24Vdc (300mA)

Pilot Monitor with ATEX Enclosure for Closely Spaced Flares or Mounting Distances Greater then 1500ft/457m

F	  1		PM-70-A-ATEX							$8,200		4 - 6 weeks

Description:		Dual-wavelength visual aiming pilot monitor with internal display

and user interface, signal conditioning and system diagnostics.

in NEMA 7 housing. Includes sealed junction box

with screw terminals attached to housing for field wiring.

Measuring range:	0 - 100 %

Field of View:		70:1 optics, 14ft diameter @ 1000ft distance ( 4.2m @ 305m )

Sensor Output:		A:  Stand Alone Sensor set to Analog Output. Provides  linear

( field selectable ) 	mA Output and SPST relay output.

( select D  for Stand Alone Sensor set to RS485 Digital Comms for

operation with the Interface Module accessory, see Options below )

Mounting included:	Swivel Bracket

Input Power:                    Sensor requirements: 24Vdc (300mA)

Optional Accessories  for above items  – add  IM or PSN4 to part number  if required

Item	Qty

G	  1		IM								$700	$700	1 - 2 weeks

Description:        	Interface Module with two displays, two mA outputs, two SPDT Relays, 				                   one TTL Relay, 90-260Vac power input, 24Vdc output to power sensor.

Communicates with  sensor via RS485 in lieu of the mA and single

relay output from the sensor when Stand Alone Analog mode.

Item	Qty

H	  1		PSN4								$300	$300	1 - 2 weeks

# Description:		Power Supply in NEMA 4X (IP65) Enclosure

Input:  90-260Vac, Output 24Vdc to power one sensor.

Consult factory for options regarding interconnect electrical cable

lengths and mounting accessories.  Williamson sensors are “Made in USA”

Please refer to the appropriate brochure and/or data sheet for additional specifications.

NOTE:  One instruction manual is included with each instrument.  Additional printed manuals are available for $25.00 each.  For Domestic shipments, shipping terms are FOB Concord MA.  For International shipments, shipping terms are INCOTERMS FCA Concord MA, USA. Payment Terms are Net 30 Days.  This quote is valid for 45 days.  Details of two-year warranty are provided in the product manuals.  Applicable taxes, duties or transportation fees have not been included.

________________________

By:

Title:

Tel:

E-Mail: